## Slide 1
DCT-Enhanced
Lithography Hotspot
Detection
A Controlled Spatial-Frequency Study on ICCAD-12 Benchmarks DA-2 Assignment
Palempalli Lakshmi Narasimha — 23BVD1007
A. Sanjay — 23BVD1012
Anish Anil Shende — 23BVD1013
Vellore Institute of Technology, Chennai, India
2-D DCT coefficient plane: DC / low frequency (top-left) → high frequency

## Slide 2
Some layout patterns fail to print: hotspot detection finds them early
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
2
Layout
Rasterised design clip
Lithography process
Sub-wavelength printing effects
Printed result
Some geometries print poorly
Hotspot detection
Flag failing patterns early
Typical hotspot geometries
Narrow necks
Tight corner-to-corner spacings
Isolated line ends
Dense 2-D interactions
Why a machine-learning surrogate?
Full lithography simulation
Most faithful, but too expensive for repeated full-chip verification
ML-based hotspot detection
Learns from labelled layout clips: a faster surrogate detector
A single hotspot can reduce yield across an entire wafer lot, so hotspot identification is a mandatory physical-verification step.

## Slide 4
Research question and hypotheses
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
4
RESEARCH QUESTION
Can frequency-domain information from the DCT improve hotspot detection compared with a spatial representation, with classifier capacity, training schedule and benchmarks fixed?
H1
Information
DCT-derived representations contain discriminative information that a lightweight CNN can exploit.
H2
Band separation
Separating DCT coefficients into frequency bands improves representation quality over undifferentiated full-spectrum DCT.
H3
Fusion
Combining spatial and frequency information provides complementary evidence and improves detection.
Hypotheses were formulated before the comparison and are treated as falsifiable: the experiments test them rather than assume them.

## Slide 5
Controlled design: one lightweight CNN, four representations, five benchmarks
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
5
ICCAD-12 benchmarks B1–B5
224 × 224 grayscale layout clips
Four representations (R0–R3)
Same lightweight CNN budget
Held-out official test sets (untouched)
BA · Precision · Recall · Specificity · F1
5
benchmarks (B1–B5)
12,873
trainable parameters
Nadam
optimiser
10
epochs
32
batch size
BCE
binary cross-entropy loss
Deliberately not applied: class weighting, resampling, augmentation, threshold tuning. Each representation shows its raw behaviour under an identical, unmodified recipe.

## Slide 6
Four representations, one fixed CNN
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
6
R0
Spatial baseline
Grayscale clip
Resize 224 × 224
Normalise (÷ 255)
Replicate to 3 channels
R1
Full DCT
Grayscale clip
2-D DCT
Magnitude |·|
log1p
Min–max (per image)
Replicate to 3 channels
R2
Multi-band DCT
2-D DCT
Magnitude |·|
log1p
Min–max (per image)
Radial bands LOW / MID / HIGH
3 channels
R3
Spatial + DCT fusion
Spatial branch
10 filters
Multi-band DCT branch
5 filters
Feature fusion (concatenate)
Dropout → Dense 64 → sigmoid
All configurations: 12,873 trainable parameters.

## Slide 7
Severe class imbalance makes ordinary accuracy misleading
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
7
Chart: Hotspot share of official test clips (%)
| B1 | B2 | B3 | B4 | B5 | Overall
Hotspot share (%) | 4.61 | 1.19 | 3.76 | 0.55 | 0.21 | 1.88
Why ordinary accuracy fails
Labelling every clip non-hotspot gives 99.79% accuracy on B5 while detecting nothing.
PRIMARY METRIC
BA = (Recall + Specificity) / 2
Weights both classes equally; any constant classifier scores exactly 50%.
146,277 test clips, of which only 2,750 are hotspots (1.88%)

## Slide 8
Band separation substantially improves DCT, but spatial representation remains stronger
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
8
Chart: Average balanced accuracy, B1–B5 (unweighted mean, %)
| R0 Spatial | R1 Full DCT | R2 Multi-band DCT | R3 Spatial + DCT
Average BA | 92.46 | 51.54 | 64 | 64.61
A constant classifier scores 50%.
Change in average BA (percentage points)
R1 vs R0
−40.92 pp
R2 vs R1
+12.46 pp
R3 vs R2
+0.61 pp
R3 vs R0
−27.85 pp

## Slide 9
Benchmark-wise: spatial is stable, DCT-based models are benchmark-dependent
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
9
Chart: Balanced accuracy per benchmark (%)
| B1 | B2 | B3 | B4 | B5
R0 Spatial | 95.02 | 97.05 | 93.55 | 82.84 | 93.82
R1 Full DCT | 50 | 52.1 | 50.18 | 55.42 | 49.99
R2 Multi-band DCT | 50 | 79.8 | 86.55 | 50.01 | 53.66
R3 Spatial + DCT | 92.42 | 50 | 53.84 | 49.99 | 76.82
R0 stays ≥ 82.84%
on every benchmark (range 82.84–97.05%)
DCT-based models
show strong benchmark dependence and several degenerate operating points near 50% BA.
R2: 50.00–86.55%
R3: 49.99–92.42%
R2 best on B2/B3; R3 best on B1/B5

## Slide 10
B3 confusion matrices: balanced accuracy alone hides how each model fails
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
10
R0 — Spatial
Pred NHS
Pred HS
Actual
NHS
Actual
HS
41,128
TN
5,205
FP
30
FN
1,778
TP
Recall 98.34% · Spec. 88.77%
Most balanced behaviour
R1 — Full DCT
Pred NHS
Pred HS
Actual
NHS
Actual
HS
168
TN
46,165
FP
0
FN
1,808
TP
Recall 100.00% · Spec. 0.36%
Flags almost everything as hotspot
R2 — Multi-band DCT
Pred NHS
Pred HS
Actual
NHS
Actual
HS
35,610
TN
10,723
FP
68
FN
1,740
TP
Recall 96.24% · Spec. 76.86%
High recall, but many false alarms
R3 — Spatial + DCT
Pred NHS
Pred HS
Actual
NHS
Actual
HS
46,175
TN
158
FP
1,663
FN
145
TP
Recall 8.02% · Spec. 99.66%
Rejects almost everything
Recall vs. specificity: a missed hotspot (FN) propagates to mask and wafer, while a false alarm (FP) costs simulation or inspection time. Higher specificity alone is not better: R3 has the highest specificity but recovers only 8.02% of hotspots. On B3 the ranking is R0, then R2, then R3.

## Slide 11
B3 ablation: only the MID band works alone, and combining bands adds 19.45 pp
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
11
Chart: B3 balanced accuracy (%)
| Spatial R0 | Full DCT R1 | Multi-band R2 | LOW only | MID only | HIGH only
BA | 93.55 | 50.18 | 86.55 | 50 | 67.1 | 50.6
B3 only. MID is the best individual band on B3; no universal band ordering is implied.
+19.45 pp
multi-band (86.55%) vs best single band, MID (67.10%)
LOW only
All-negative: 0% recall, 100% specificity
MID only
Only non-degenerate single band: 98.34% recall, 35.87% specificity
HIGH only
Near all-positive: 100% recall, 1.19% specificity
LOW + MID + HIGH
Specificity 35.87% → 76.86%; recall 98.34% → 96.24%

## Slide 12
Frequency features can be class-separable even when the CNN fails
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
12
Chart: Feature-level univariate AUC (descriptive)
| B1 | B2 | B3 | B4 | B5
High-band energy ratio | 0.5456 | 0.6038 | 0.7904 | 0.8356 | 0.8308
Spatial mean | 0.7392 | 0.8178 | 0.6577 | 0.6578 | 0.6493
Low-band energy ratio | 0.6442 | 0.5903 | 0.5348 | 0.5498 | 0.5486
Axis starts at 0.5 (chance level for AUC). On B1–B2, intensity-related descriptors are strongest.
FEATURE LEVEL
High-band energy ratio, AUC up to 0.8356 on B3–B5
≠
CLASSIFIER LEVEL
HIGH-only CNN on B3: 50.60% balanced accuracy
Useful frequency information exists, but the evaluated representation and preprocessing do not let the CNN exploit it robustly. Feature AUC is not CNN performance.

## Slide 13
Frequency-domain models are not cheaper here; conclusions stay within scope
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
13
Chart: Training time (s), B2–B5
| B2 | B3 | B4 | B5
R0 Spatial | 607.51 | 650.96 | 545.71 | 302.81
R1 Full DCT | 923.47 | 955.72 | 764.53 | 454.37
R2 Multi-band | 947.84 | 840.37 | 750.28 | 445.05
R3 Spatial + DCT | 1306.4 | 1395.71 | 1466.99 | 653.47
R3 is the most expensive configuration: on B2–B5 training and at inference on all five benchmarks; inference is about 2× R0 on B2–B5 (B3: 384.95 s vs 155.89 s). Timings come from one uncontrolled environment: relative cost only.
Methodological limitations
R0/R1: 80/20 train/validation split; R2/R3 and B3 ablations: full training partition, no validation subset
Timing collected in one environment
One lightweight architecture and one set of band boundaries (r = 0.15, 0.40)
Single runs: no seed variance or significance tests
Do not generalise to all DCT representations or architectures

## Slide 14
Conclusion
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
14
DCT contains useful information, but the tested DCT representations do not provide a robust improvement over the spatial representation.
92.46%
R0 Spatial · average BA
51.54%
R1 Full DCT · average BA
64.00%
R2 Multi-band · average BA
64.61%
R3 Spatial + DCT · average BA
Multi-band structure clearly improves over full DCT.
B3 ablation: the bands carry complementary information.
Feature-level separability does not automatically translate into effective CNN classification.
Representation design and preprocessing matter as much as the transform itself.
Future work: learnable frequency representations, adaptive band boundaries, normalisation strategies that preserve absolute spectral information, and stronger architectures.

## Slide 15
Work distribution
DCT-Enhanced Lithography Hotspot Detection | VIT Chennai
15
Collaborative research responsibilities
Palempalli Lakshmi Narasimha
23BVD1007
Literature review and problem formulation
ICCAD-12 dataset preparation and analysis
Spatial baseline (R0) implementation and evaluation
Related-work analysis
Documentation
A. Sanjay
23BVD1012
DCT preprocessing and representation design
Full-DCT (R1) and Multi-band DCT (R2) implementation
Frequency-band ablation
Feature-level AUC analysis
Experimental result analysis
Anish Anil Shende
23BVD1013
Spatial-frequency fusion (R3) implementation
Model architecture and parameter matching
Benchmark-wise evaluation and confusion-matrix analysis
Computational-cost analysis
Visualization and presentation preparation
Experimental design, interpretation, manuscript preparation, and final review were conducted collaboratively by all team members.